## Slide 1: Spectrum measurement & channel capacity
Prepared By:
Tawsif Ahmad Luvpreet Kaur Thakur Bhattarai

## Slide 2
Equipments used
Software:
        SDR SHARP v1.0.0.1700
Hardware:
        NooElec R820T2 SDR

## Slide 3
Spectrum of Interest
In project 1, we worked on Wi-Fi wireless standard
Wi-Fi works on 2.4 GHz bands (2.412 GHz – 2.484 GHz)
We received some signals in this frequency range
Some of them has been presented in the upcoming slides
We used RF gain 38.6 dB in SDRSHARP

## Slide 4
Calculations
Noise Floor, N1 = -120 dBm
Noise floor in Sdrsharp without any valid signal: N2
Power gain of the software: G = N2 – N1
Peak of the valid signal: A
Received power: P = A – G
SNR: A – N2

## Slide 5
AT 2472376680 Hz
N2 = -59.3 dBm
G = -59.3 + 120 = 60.7 dB
A = -17.1 dBm
P = -17.1 – 60.7 = -77.8 dBm
SNR = 42.2 dB

## Slide 6
AT 2447998180 Hz
N2 = -56.7 dBm
G = 63.3 dB
A = -19.8 dBm
P = -83.1 dBm
SNR = 36.9 dB

## Slide 7
AT 2463997540 Hz
N2 = -57.5 dBm
G = 62.5 dB
A = -16.5 dBm
P = -79 dBm
SNR = 41 dB

## Slide 8
Some Observations
The photos here are shown for active signal transmission
When there are no signal transmission, the spikes are a lot smaller.
If we look at the spectrum band at a different place, for example, we tried at the University Union, we got spikes in different frequencies.

## Slide 9
Channel Capacity
We considered WHRW-FM 90.5 MHz Radio which is conducted by Binghamton University
The test was done in 109 Schubert Street, Binghamton, NY.
Transmission distance, d = 2.6 miles = 4184.3 m.
Transmitter power = 1450 watts = 61.614 dBm
Wavelength = 3.315 m (approximately)
We used no RF gain in the software

## Slide 10
FM Signal Measurement
N2 = -61.9 dBm
G = 58.1 dB
A = -39.5 dBm
Pr = -97.6 dBm
SNR = 22.3 dB

## Slide 11
Free Space Path Loss Model
Here, G is antenna gain which is assumed to be 1.
d is the distance between transmitter and receiver = 4184.3 m
Pt = 1450 watts
So, using the model we get Pr = -22.4 dBm which is very far from the measured value.
So, we cannot fit this data with the free space path loss model

## Slide 12
Two Ray Model
Transmitter height = 80 m (from the web)
Receiver height = 6 m and d = 4184.3 m
We get Pr = -29.63 dBm
Which is lot less than the observed value. So, this model doesn’t fit too.

## Slide 13
Simplified Path Loss Model
Where, and we assume
We get, K = -31.58 dB
Using Trial and error, we set = 4.8 to obtain
Pr = -95.77 dBm
which is closer to the measured value of -97.6 dBm
SNR = -95.77 dBm + 120 dBm = 24.23 dB

## Slide 14
FM Signal Measurement 2
N2 = -60.9 dBm
G = 59.1 dB
A = -37.1 dBm
Pr = -96.2 dBm
SNR = 23.8 dB

## Slide 15
FM Signal Measurement 2
N2 = -63.8 dBm
G = 56.2 dB
A = -39.1 dBm
Pr = -95.3 dBm
SNR = 24.7 dB

## Slide 16
Observations
We see that, all of the signals power are close to the value obtained from the simplified path loss model with K = -31.58 dB and = 4.8
Observed SNRs ( 22.3 dB, 23.8 dB & 24.7 dB) are close to the SNR obtained from the model (24.23 dB)
When news was being played over the radio the power is lower than that of the music.

## Slide 17
Capacity measurements
1st observation: SNR = 22.3 dB; we get C = 1.04 Mbps
2nd observation: SNR = 23.8 dB; we get C = 1.10 Mbps
3rd observation: SNR = 24.7 dB; we get C = 1.15 Mbps
From the model: SNR = 24.23 dB; we get C = 1.12 Mbps
We can see that the capacity of the observations are close to the capacity obtained from the model.
with B = 140 kHz

## Slide 18
THANK YOU